The Safety Reset
A Post-Attack Recovery Architecture for Smart Electricity Meters
Eine Architektur zur Kontrollwiederherstellung nach Angriffen auf Smart Metering in Stromnetzen

---
Fundamentals [4m]

---
Structure of the electrical grid
- Transmission lines
- Generators
- Loads
- Transformers
- Switchgear

---
The role of smart meters

---
Smart meter functions
  - High-res Load measurement
  - Load switching
  - Delinquent disconnect
  - Smart home gateway (lol)

---
The motivation
  - Load forecasting
    - The energy market
    - Accurate forecasting reduces cost
  - Profit maximization
    - Pass-through of costs
  - Selling data
  - Cronyism
    - Nobody asked for this

---
Smart metering regulation
  - Intl standards: Comms interfaces

---
Physical structure
  - Measurement Transformer (MT)
  - Main app MCU
  - Comms MCU
  - Load switches
  - Display/UI
  - DE vs. the rest of the world

---
Security in the distribution grid
  - Firmware is everywhere
  - Firmware is haaard
    - L+G spends 36% of their R&D budget on SW
  - The state of embedded security
    - everybody fails
    - case in point: apple T2
    - µCs: lack in modern security features

---
Endpoint safety & security [3m]

---
Prototypical attackers
  - Customers: Electricity theft
    - Also sold as a service by organized crime
  - Bored teenagers
  - State actors

---
System structure and security
  - Exploiting centralized control
  - Communication channels exploits
  - Control function exploits
  - Endpoint exploits

---
Complex hard- and firmware
  - The line between µC and SoC is blurring
  - Complex HW functions
    - DMA
    - MMUs/MPUs
    - Coprocessors and Enclaves
  - Firmware is even worse
  - Complex HW/FW bundles are integrated
    - Most common: radio modems
    - Also: AI accelerators
    - Also: Complex sensors (e.g. camera/barcode)

---
The safety reset [2m]
- System function
  - Hard firmware reset
  - Re-flash using JTAG
  - Golden image: Known-good, all network comms disabled
    - → True Fail-Safe
- Remote Trigger
  - Broadcast comms channel for quick response
  - Robust channel: should not go down along with grid

---
Grid-associated comms channels [4m]
- Powerline Communication (PLC)
  - Transmit at higher frequencies through grid wiring
  - Rundsteuerung: ~300Hz / 10Bd / 50km
  - Narrowband: ~100kHz / 100kBd / 1000m
  - Broadband: ~100MHz / 1Gbit / 50m
- Landline IP
  - POTS/DSL
  - Fiber
- Wireless IP
  - Cellular 2G/3G/4G/5G
  - WiMAX etc.
  - Proprietary
  - SatComm
- Short-range wireless
  - 802.15.4 family
  - Proprietary
  - Frequencies: 2.4GHz, sub-1GHz
- → None of these work for us: too expensive or not reliable under attacks

---
The Hack: Grid Frequency Modulation (GFM)
- Grid frequency is load balance dependent
  - Generators/Transmission lines act like spring-coupled oscillators
- Apply a large load, f drops
- Modulate a large load to control Δf

---
Constructing a reliable GFM comms channel [6m]

---
Channel properties
- Noisy, ultra-narrowband
- Global with phase delay

---
Modulation
- Poor SNR makes UWB necessary
- Can’t be too complex: DSSS is a good compromise
- Long integration times (minutes)
- Accurate frequency measurement is a limiting factor

---
ECC
- Small block size
- Code size limitation
- Can be simple: Efficiency is good, but not critical

---
Cryptography
- Non-standard threat model
- Simple setup
- A trivial custom solution is justifiable to save transmission bandwidth

---
Testing and validation [3m]

---
Conclusion [2m]

---
Tangible products [1m]
- The demonstrator
- Extensive simulation notebooks
- Prototype firmware
- Firmware code size analysis tool
- → All Open Source!!

---
Questions